P.S.R. ENGINEERING COLLEGE SIVAKASI-626 140

(An Autonomous Institution, Affiliated to Anna University, Chennai)

QUESTION BANK

| Programme: | B.E. | Branch | Electronics and Communication Engineering |
| --- | --- | --- | --- |
| Acad. Year: | 2018-2019 | Year/Semester | II Yr/III Sem |
| Course Code: | 161EC31 | Course Name | ANALOG ELECTRONIC CIRCUITS |
| Course Tutor: | Sec I : Dr.P.Marichamy (Dean) Sec II: Ms.M.Vimala AP/ECE |

UNIT-I	REVIEW OF DIODE AND TRANSISTOR – CHARACTERISTICS AND BIASING

PART - A

|  | Define biasing. What is the need for biasing? |
| --- | --- |
|  | What are the advantages of self bias over other types of biasing? |
|  | Define Forward recovery time. |
|  | What is thermal runaway? |
|  | What are all the factors that affect the Q-point of a circuit using BJT? What is its effect? |
|  | Show the circuit diagram of fixed bias single stage transistor circuit |
|  | Determine the collector current and base current for the fixed bias configuration using the specifications β=50, RB=300KΩ, VCC=9v, RC=2KΩ, VBE=0.7v. |
|  | How the switching time of transistor is reduced? |
|  | How will you reduce the recovery time? |
|  | What are all the categories of Diode equivalent Circuit? |

PART- B

|  | Explain the switching characteristics of PN diode | 16 |
| --- | --- | --- |
|  | Discuss in detail about Diode equivalent Circuit. | 16 |
|  | (i)Determine the Q-point for voltage divider bias circuit with R1=56KΩ, R2=12.2KΩ, RC=2KΩ, RE=400Ω, VCC=10v, VBE=0.7v and β=150. | 10 |
|  | (ii)Determine the DC value of IC and VCE of a fixed bias circuit with RB=110KΩ, RC=520Ω, VCC=12v and β=120. | 06 |
|  | Estimate the stability factors for voltage divider biasing | 08 |
|  | Explain about fixed bias operation of a transistor circuit with diagram. | 08 |
|  | Determine the operating point in a voltage divider biased transistor circuit with the specification as: R1=10KΩ, R2=5.6KΩ, RC=1KΩ, RE=560Ω, VCC=10v and β=100. | 16 |
|  | (i) Distinguish between CE, CB and CC amplifiers. | 08 |
|  | (ii) Discuss how AC and DC load lines are drawn? | 08 |

UNIT-II     	BJT AND JFET FREQUENCY RESPONSE

PART – A

|  | Define the term logarithm and decibels. |
| --- | --- |
|  | Express Miller effect capacitance |
|  | Define Frequency Response of an amplifier |
|  | What is meant by multistage Amplifier? |
|  | Draw the general shape of the frequency response of amplifier |
|  | What is the difference between single stage and multistage amplifier? |
|  | Write an expression for the bandwidth of multistage amplifier. |
|  | Give two advantages of common source FET amplifier? |
|  | Write the relation between the bandwidth and rise time of an amplifiers? |
|  | What are the coupling methods used for coupling in multistage amplifiers? |

PART- B

|  | Explain the High frequency response of BJT & FET amplifier | 16 |
| --- | --- | --- |
|  | Illustrate the Miller effect capacitance. Assess the expression for Input capacitance and output capacitance | 16 |
|  | Explain the Low frequency response of BJT & FET amplifier | 16 |
|  | Evaluate the fHi , fHo , fβ , fT using the High frequency Response network RS = 1KΩ, R1 = 40KΩ, R2 = 10KΩ, RE = 2KΩ, RC = 4KΩ, RL = 2.2KΩ, CS = 10µF, CC = 1µF, CE = 20µF, CWi = 6PF, CWo = 8PF, β=100, r0 = ∞Ω, VCC = 20V, Cbe = 36PF, Cbc = 4PF, Cce = 1P.F | 16 |
|  | Explain in detail about the Multistage frequency Effects | 8 |
|  | Elaborate in detail about the low frequency of BJT amplifier | 8 |

UNIT-III	GENERAL AND FEEDBACK AMPLIFIERS

PART - A

|  | What is a Darlington connection in the amplifiers? |
| --- | --- |
|  | Define bootstrapping in feedback amplifiers. |
|  | What is meant by feedback and what are the types of feedback? |
|  | Justify that negative feedback amplifier increases bandwidth. |
|  | What are the characteristics of negative feedback? |
|  | Show the schematic diagram of series and shunt mixing. |
|  | If an amplifier has a gain of 400 and feedback ratio is 0.1.Find the gain with negative feedback. |
|  | What is cascade amplifier? |
|  | What are the effects of negative feedback in amplifiers? |
|  | What are the applications of Darlington amplifier? |

PART- B

|  | Illustrate the cascade amplifier and explain its working principle | 06 |
| --- | --- | --- |
|  | Briefly explain the operation of Darlington emitter follower and also derive an expression for Current gain, Voltage gain. | 10 |
|  | Show the block diagram of voltage series and current shunt feedback amplifiers and derive the expressions for input impedance Rif and output impedance Rof. | 16 |
|  | Show the circuit diagram of a voltage series feedback and analyze the circuit to determine the gain, input resistance and output resistance with and without feedback. | 16 |
|  | Develop the design procedure for the feedback amplifier | 10 |
|  | Illustrate the working principle of cascade amplifier with neat diagram | 6 |

UNIT-IV	POWER AMPLIFIERS

PART - A

|  | List any two advantages of transformer coupled class A amplifier circuit |
| --- | --- |
|  | Calculate the effective resistance RL’ seen looking into the primary of a 10:1 transformer connected to an output load of 16Ω. |
|  | Define conversion efficiency. |
|  | What is meant by cross over distortion? How it can be eliminated? |
|  | What are the disadvantages of complementary symmetry power amplifier? |
|  | In a class B amplifier VCE(min)=2v and a supply voltage Vcc=15v.find the collector circuit efficiency. |
|  | List the classification of large signal amplifiers? |
|  | What are the advantages and disadvantages of Class B Power amplifier |
|  | Define Tuned amplifier. |
|  | What is meant by Power amplifier? |

PART- B

|  | Explain the operation of Class B complementary symmetry push pull amplifier and derive its efficiency | 16 |
| --- | --- | --- |
|  | Show the circuit of a transformer coupled class A amplifier and explain how conversion efficiency is improved using the circuit. | 16 |
|  | What is distortion in an amplifier and discuss about different types of distortion in power amplifiers? | 16 |
|  | Briefly explain the operation of Class B push pull power amplifier and derive its efficiency | 16 |
|  | Elaborate in detail about the single tuned amplifier with neat diagram | 8 |
|  | Illustrate the working principle of series fed Class A power amplifier. | 8 |

UNIT-V	OSCILLATORS

PART - A

|  | Define Oscillator. |
| --- | --- |
|  | What are the classifications of Oscillators? |
|  | Define Barkhausen Criterion |
|  | What are the different types of feedback oscillators? |
|  | If L1=1mH,L2=2mH and C=0.1nF,what is the frequency of oscillation of the Hartley oscillator? |
|  | What are advantages of Wien bridge oscillator? |
|  | Why Mono stable Multi vibrator is called as gatting circuit? |
|  | What are the uses of Crystal Oscillators? |
|  | What are the advantages of Mono stable Multi vibrator? |
|  | What are the applications of Schmitt trigger? |

PART- B

|  | Develop the working of Hartley oscillator and derive the expression for frequency of oscillation .. | 16 |
| --- | --- | --- |
|  | Derive the expression for general form of an LC oscillator and also Explain the operation of Colpitts oscillator and derive the expression of its frequency of oscillation. | 16 |
|  | Explain the operation of RC phase shift oscillator with a neat circuit diagram and derive the expression of frequency of oscillation . | 16 |
|  | With neat circuit diagram and suitable wave forms, explain the operation of a collector coupled transistor monostable multivibrator. | 16 |
|  | (i) Explain the working principle of Schmitt trigger circuit with neat diagram | 08 |
|  | (ii) Elaborate in detail about the operation of UJT Relaxation Oscillator | 08 |